## Slide 1: Flood risk assessment in Limbe (Cameroon) using a GIS weighed sum method
BY Lucy Deba Enomah

## Slide 2: Introduction
Coastal zones pull factors
  Rich natural resources that support subsistence
  Logistical reasons
  Recreational, socio-economic and cultural activities
Rapid population growth and urbanization in coastal areas in Africa
Increased Risk of dangerous and costly flooding in coastal regions
  Climate Change
  Urbanization
  Land subsidence

## Slide 3: Introduction Cont’d
Uncontrolled urban growth settlement
Risk zonation policy developed to manage flood is bureaucratic and financially burdensome
  Lack of adequate information due to limited technical skills
  Lack of adequate resources (financial and material).
Flood prevention is of utmost important to coastal cities.
GIS has been successfully used to visualize the scale of flooding as well as to evaluate flood maps to generate flood damage assessment maps and flood risk maps

## Slide 4: Study area
Location: Southwest Region
Elevation: 458m
Two seasons: Dry (Nov to march) and rainy (April to Oct)
Main Rivers: Limbe River and Ejengele
Average annual temperature: 26°C
Annual rainfall average is 2000 mm and peak average rainfall of 3000 mm

## Slide 5: Methodology

## Slide 6: Factors

## Slide 7: Factor interactions
 | Soil texture | LULC | Slope | Elevation | Precipitation | Flow Accumulation
Soil Texture | No effect | Major | No effect | No effect | No effect | Major
LULC | No effect | No effect | Minor | No effect | Major | Major
Slope | Minor | Major | No effect | No effect | No effect | Major
Elevation | Major | Major | Minor | No effect | Major | Major
Precipitation | major | Minor | No effect | No effect | No effect | Major
Flow Accumulation | No effect | Major | Minor | No effect | No effect | No effect

## Slide 8: Factor Weights
LULC
Flow Accumulation
Slope
Precipitation
Elevation
Soil texture
 | Interaction Btw Factors | Rates | Product
Soil Texture | 2 major + 0 minor | (2*1)+(0*0.5) | 2
LULC | 2 major + 1 minor | (2*1)+(1*0.5) | 2.5
Slope | 2 major + 1 minor | (2*1)+(1*0.5) | 2.5
Elevation | 4 major + 0 minor | (4*1)+(0*0.5) | 4
Precipitation | 2 major + 1 minor | (2*1)+(1*0.5) | 2.5
Flow Accumulation | 1 major + 1 minor | (1*1)+(1*0.5) | 1.5

## Slide 9: Statistical analysis of Flood risk zones
Flood zones | Values
Very Low | 4.47 km2
Low | 8.58 km2
Medium | 10.81 km2
High | 11.32 km2
Very high | 13.36 km2

## Slide 10: Flood Risk zones and Landuse
 | LULC Classes |  | 
Flood Risk Zones | Urban/Residential | Forest/oil Palms | Farmland
Very Low | 0.3 | 6.5 | 22.4
Low | 3.5 | 24.0 | 37.4
Medium | 14.5 | 33.6 | 25.0
High | 33.8 | 25.8 | 11.8
Very High | 47.8 | 10.0 | 3.6

## Slide 11: Impact Analysis of Flood Risk Zones

## Slide 12: Conclusion
This study was conducted to assess the effectiveness of remote sensing and GIS for Flood risk zones mapping.