## Slide 1
Spatiotemporal Traffic Database Construction and Congestion Pattern Analysis
Using Online Traffic Maps: A Case Study of Metropolitan Atlanta, Georgia, U.S.A.
Authors
Jeong Chang Seong | University of West Georgia
Hyeokjin Hong | Kyunghee University
Seorim Cho | Kyunghee University
Ana Stanescu | University of West Georgia
Chul sue Hwang | Kyunghee University
Presented by
Hyunmin Kim | Kyunghee University
| Geography, GIS
| Department of Geography
| Kyunghee University, Seoul, Korea
| earth940709@khu.ac.kr
2022 AAG Annual Meeting

## Slide 2
Pollutants From Cars
PAGE 2
Research Topic
Data
Analysis & Result
Conclusion
Introduction
Traffic Delay in Major Cities
INRIX, 2018
🚗
67 min
Americans' Eating Patterns and Time Spent on Food: The 2014 Eating & Health Module Data. USDA
🍴
≒
66 min
National Household Travel Survey,2017
Time Spent per Day

## Slide 3
Individual's Response to Traffic Congestion
PAGE 3
Research Topic
Data
Analysis & Result
Conclusion
Introduction
Traffic Pattern
Recurring
55 %
Recurrent Traffic Congestion
Non
recurring
45 %
insufficient capacity
unrestrained demand
ineffective management of capacity
DOT, 2019
<

## Slide 4
PAGE 4
Data
Analysis & Result
Conclusion
Introduction
Research Topic
Using the Google traffic image to build a traffic database
Research Objectives
Develop new method for collecting congestion data
&
Analyzing traffic congestion patterns
Change in the frequency of congestion by day
Analysis of major congestion points
Congestion pattern extraction and visualization

## Slide 5
What traffic data was used?
- Annual Average Daily Traffic(AADT)
Sensor-based data collection for traffic research
PAGE 5
Data
Analysis & Result
Conclusion
Introduction
Research Topic
limited
collection points
Maintenance
cost
Former Research about Traffic Pattern (Seong et al., 2011)
Automatic Traffic Recorders(ATRs)
- Predict traffic volume or traffic congestion

## Slide 6
What is Floating Car Data?
Estimating traffic condition from crowd location data
PAGE 6
🚗
🚗
🚗
🚗
🚗
🚗
GPS Signal
Time
Location
Data
Processing
Traffic Volume
Speed
Data
Analysis & Result
Conclusion
Introduction
Research Topic

## Slide 7
Research Area
PAGE 7
https://www.volpe.dot.gov/news/how-much-time-do-americans-spend-behind-wheel
UT
WY
GA
NM
OK
IN
MS
ND
FL
DC
WV
ID
MN
NV
WI
MO
NC
AL
TX
HI
TN
MD
MT
OH
CA
VA
MI
AZ
KY
MA
KS
ME
NI
NY
CO
DE
AH
LA
IL
SC
IA
CT
VT
OR
RI
WA
NE
SD
NH
PA
AK
1.6
1.4
1.2
1.0
0.8
0.6
0.4
0.2
0.0
Atlanta, one of the world's
10 worst cities for congestion
(INRIX, 2016-2017)
Research Area
Metro Atlanta
Georgia County
Daily Auto Travel per Licensed Driver
2015 National Household Travel Survey
2014
2015
GA ranked third in the Daily
Auto Travel per Licensed Driver in the US
States
Average
57min
<
73 min
GA
NY
LA
SF
GA
……
Data
Analysis & Result
Conclusion
Introduction
Research Topic

## Slide 8
PAGE 8
https://www.volpe.dot.gov/news/how-much-time-do-americans-spend-behind-wheel
Heavy Congestion
R : 129 | G : 31 | B : 31
Moderate Congestion
R : 242 | G : 60 | B : 50
No Congestion
R : 100 | G : 215 | B : 110
Low Congestion
R : 255| G : 150| B : 80
The level of congestion indicated by
the color of the traffic information
Research Topic
Analysis & Result
Conclusion
Introduction
Data
How to Use Google Traffic Data?
How to extract data from Google traffic information images

## Slide 9
1. Data collection
PAGE 9
2. Extract Traffic Congestion Information
3. Create 3D Spatiotemporal Dataset
Collect Snapshot every 10 minutes
Snapping Google Maps image
From September 25 to October 22th, 2021 (28 Days)
1 Day (144 Image) -> 4 Weeks (5032 Image)
Create a masking layer along the road Pixel
Extract the RGB value of each image pixel
Convert extracted pixel RGB to Congestion Index(CI)
Stack each time layers to create 3D Spatiotemporal data
Python Numpy’s multi-dimensional array structure
X axis : Longitude / Y axis : Latitude / Z axis : Time
Latitude
Longitude
Scale
Traffic Layer
https://www.google.com/maps/@39.1269755,-77.1876252,12z/data=!5m1!1e1/
Research Topic
Analysis & Result
Conclusion
Introduction
Data

## Slide 10
1. Data collection
PAGE 10
2. Extract Traffic Congestion Information
3. Create 3D Spatiotemporal Dataset
Create a masking layer along the road Pixel
Extract the RGB value of each image pixel
Convert extracted pixel RGB to Congestion Index(CI)
Stack each time layers to create 3D Spatiotemporal data
Python Numpy’s multi-dimensional array structure
X axis : Longitude / Y axis : Latitude / Z axis : Time
Research Topic
Analysis & Result
Conclusion
Introduction
Data
Collect Snapshot every 10 minutes
Snapping Google Maps image
From September 25 to October 22th, 2021 (28 Days)
1 Day (144 Image) -> 4 Weeks (5032 Image)

## Slide 11
1. Data collection
PAGE 11
2. Extract Traffic Congestion Information
3. Create 3D Spatiotemporal Dataset
Create a masking layer along the road Pixel
Extract the RGB value of each image pixel
Convert extracted pixel RGB to Congestion Index(CI)
Stack each time layers to create 3D Spatiotemporal data
Python Numpy’s multi-dimensional array structure
X axis : Longitude / Y axis : Latitude / Z axis : Time
Research Topic
Analysis & Result
Conclusion
Introduction
Data
Collect Snapshot every 10 minutes
Snapping Google Maps image
From September 25 to October 22th, 2021 (28 Days)
1 Day (144 Image) -> 4 Weeks (5032 Image)

## Slide 12
1. Data collection
PAGE 12
2. Extract Traffic Congestion Information
3. Create 3D Spatiotemporal Dataset
Create a masking layer along the road Pixel
Extract the RGB value of each image pixel
Convert extracted pixel RGB to Congestion Index(CI)
Stack each time layers to create 3D Spatiotemporal data
Python Numpy’s multi-dimensional array structure
X axis : Longitude / Y axis : Latitude / Z axis : Time
Research Topic
Analysis & Result
Conclusion
Introduction
Data
Collect Snapshot every 10 minutes
Snapping Google Maps image
From September 25 to October 22th, 2021 (28 Days)
1 Day (144 Image) -> 4 Weeks (5032 Image)

## Slide 13
1. Data collection
PAGE 13
2. Extract Traffic Congestion Information
3. Create 3D Spatiotemporal Dataset
Create a masking layer along the road Pixel
Extract the RGB value of each image pixel
Convert extracted pixel RGB to Congestion Index(CI)
Stack each time layers to create 3D Spatiotemporal data
Python Numpy’s multi-dimensional array structure
X axis : Latitude / Y axis : Longitude / Z axis : Time
Research Topic
Analysis & Result
Conclusion
Introduction
Data
Collect Snapshot every 10 minutes
Snapping Google Maps image
From September 25 to October 22th, 2021 (28 Days)
1 Day (144 Image) -> 4 Weeks (5032 Image)

## Slide 14
PAGE 14
Research Topic
Conclusion
Introduction
Data
Analysis & Result
Change in the frequency of congestion by day
Sum of congestion frequency over time
Congestion frequency over time for each day of the week

## Slide 15
PAGE 15
Research Topic
Conclusion
Introduction
Data
Analysis & Result
Morning Major Congestion Point
Evening Major Congestion Point
Analysis of major congestion points according to traffic congestion times

## Slide 16
PAGE 16
Research Topic
Conclusion
Introduction
Data
Analysis & Result
Why K-means Clustering Method?
Optimal Number of Clusters
Number of Cluster | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Silhouette Score | 0.612 | 0.51 | 0.452 | 0.417 | 0.415 | 0.38 | 0.372 | 0.365 | 0.362 | 0.354
- Data characteristic
- spatiotemporal data
- data size
- Fast
- Maximize differences between groups
- Minimize differences within groups
- Versatile
- Various data can be classified without prior information
- Inertia considers the variances of each cluster
- Silhouette coefficient reflects the variance between groups together
- Measuring Euclidean distance
- Iteratively work to minimize the distance from the center point assigned to the cluster
- Identify the structure hidden in unlabeled data by grouping similar types of data

## Slide 17
PAGE 17
Research Topic
Conclusion
Introduction
Data
Analysis & Result
Pattern 0
: Very Light All Day
Pattern 5
: Heavy Morning/Very Heavy Afternoon
Pattern 1
: Very light Daytime
Pattern 4
: Light Daytime/Heavy Congestion Lunch
Pattern 2
: Very Heavy Morning/Very light Afternoon
Pattern 3
: Very light Morning/Very Heavy Afternoon
Pattern Extraction and Visualization

## Slide 18
PAGE 18
Pattern 0
: Very Light All Day
Pattern 5
: Heavy Morning/Very Heavy Afternoon
Pattern 1
: Very light Daytime
Pattern 4
: Light Daytime/Heavy Congestion Lunch
Pattern 2
: Very Heavy Morning/Very light Afternoon
Pattern 3
: Very light Morning/Very Heavy Afternoon
Research Topic
Conclusion
Introduction
Data
Analysis & Result

## Slide 19
PAGE 19
Research Topic
Conclusion
Introduction
Data
Analysis & Result
Pattern 2
: Very Heavy Morning/Very light Afternoon
Pattern 3
: Very light Morning/Very Heavy Afternoon
Central Business District

## Slide 20
PAGE 20
Research Topic
Conclusion
Introduction
Data
Analysis & Result
Pattern 4
: Light Daytime/Heavy Congestion Lunch
Pattern 5
: Heavy Morning/Very Heavy Afternoon

## Slide 21
PAGE 21
Research Topic
Introduction
Data
Analysis & Result
Conclusion
Development of 3-D traffic congestion data collection method using Google Map Image
Collect high-resolution data for coverage of metropolitan areas.
Main congestion time of the study area & Characteristics of congestion by day of the week
The congestion pattern was analyzed through cluster analysis, and spatial analysis was presented
through visualization results.
General enough to use, without significant investment of data collection equipment or proprietary software
Efficient movement planning through congestion information for citizens
Understand the overall urban congestion phenomenon and use it as a basis for policy decisions
according to specific points
Conclusion
Discussion
Find areas where congestion occurs significantly over time and which congestion happened in an area.

## Slide 22
Spatiotemporal Traffic Database Construction and Congestion Pattern Analysis
Using Online Traffic Maps: A Case Study of Metropolitan Atlanta, Georgia, U.S.A.
2022 AAG Annual Meeting
Presented by
Hyunmin Kim | Kyunghee University
| Geography, GIS
| Department of Geography
| Kyunghee University, Seoul, Korea
| earth940709@khu.ac.kr